## Slide 1: Project Title : MRI-to-Synthetic CT Brain Scan Translation
Name: Vishal Kumar
Student Code: iitmcs_2406329
Method: Deep Learning for Medical Imaging

## Slide 2: Project Overview
The Clinical Problem
Radiotherapy planning for brain tumors currently requires both MRI (for soft tissue detail) and CT (for dose calculation). This dual-scan process is costly, time-consuming, and exposes patients to unnecessary radiation. It also introduces the risk of image registration errors.
Our Project's Goal
To develop a deep learning model that generates high-fidelity synthetic CT (sCT) scans directly from MRI images. The ultimate aim is to enable a faster, safer, and more efficient "MRI-only" clinical workflow.

## Slide 3: Project Introduction
Addresses logistical burdens in clinical workflows
Synthesizes CT from MRI using deep learning
Utilizes Pix2Pix for image-to-image translation
Optimizes G:D ratio and replacing reconstruction loss with charbonnier loss

## Slide 4: MRI vs CT Intensity Distribution & Relationship

## Slide 5: MRI with CT Boundaries Visualization

## Slide 6: Modality Contrasts (Absolute Difference=MRI_slice-CT_slice)

## Slide 7: Methods and Experiments
A series of experiments were conducted using a paired MRI-CT dataset to identify an optimal training configuration for the Pix2Pix framework. Performance was evaluated using Peak Signal-to-Noise Ratio (PSNR), Structural Similarity Index (SSIM), and Mean Absolute Error (MAE). The experimental setups are detailed below, progressing from a baseline to exploratory tests and culminating in a two-phase fine-tuning strategy.

## Slide 8: Experiment 1 : Baseline Pix2Pix
Goal: To establish the performance benchmark for a standard model.
Method: We trained the original Pix2Pix architecture using L1 loss with a 1:1 G:D ratio for a full 81 epochs.
Key Finding: This model set the "gold standard" for our project. It achieved the best overall metrics from a single training run, with a PSNR of 34.75, an SSIM of 0.954, and a low MAE of 13.22. All other experiments were measured against this strong baseline.
Experiment 2: G:D Ratio Test (2:1)
Goal: To explore if an accelerated G:D ratio could improve training speed.
Method: We trained the standard model for a short 10-epoch run but increased the generator's training frequency with a 2:1 G:D ratio.
Key Finding: This was an exploratory test that yielded a PSNR of 32.35, an SSIM of 0.930, and an MAE of 17.56. It provided a useful data point when compared to the more aggressive 3:1 ratio test, helping to inform our later, more complex experiments.

## Slide 9: Experiment 3: Two-Phase (L1 → Charbonnier)
Goal: To test if an aggressive L1 "kickstart" could effectively prime the model for a more robust Charbonnier training phase.
Method: This was a two-phase strategy. Phase 1 used L1 loss with a 3:1 ratio for 10 epochs. Phase 2 switched to Charbonnier loss with a 2:1 ratio for 35 epochs.
Key Finding: This strategy produced strong intermediate results, with a PSNR of 33.35, SSIM of 0.940, and MAE of 16.05. However, it was ultimately outperformed by our E6 strategy, suggesting that starting with Charbonnier loss from the beginning yields a better foundation.
Experiment 4: Charbonnier Test (ε=1e-4)
Goal: To evaluate the performance of the Charbonnier loss with a specific epsilon and an accelerated training ratio.
Method: We trained the model for 20 epochs using Charbonnier loss (ε=1e-4) combined with a 2:1 G:D ratio.
Key Finding: This configuration proved to be highly efficient. It produced excellent results for such a short run, with a PSNR of 33.81, an SSIM of 0.946, and an MAE of 14.68, confirming the benefits of the Charbonnier loss.

## Slide 10: Experiment 5 : Charbonnier Test (ε=1e-6)
Goal: To evaluate the Charbonnier loss with a smaller epsilon and a standard training ratio.
Method: We trained for 40 epochs using Charbonnier loss with a very small epsilon (ε=1e-6) and a stable 1:1 G:D ratio.
Key Finding: This experiment was crucial as it established the ideal "Phase 1" for our winning model. It achieved a PSNR of 32.75, SSIM of 0.937, and MAE of 16.31, showing that starting with a stable 1:1 ratio and a sharp, L1-like Charbonnier loss created the perfect foundation for later fine-tuning.

## Slide 11: Experiment 6 : Two-Phase Fine-Tuning (Winning Model)
Goal: To combine all previous insights into a definitive strategy to achieve state-of-the-art results with high efficiency.
Method: This was our winning two-phase approach. We started with the stable E5 setup for 40 epochs, then fine-tuned for 38 epochs with an accelerated 2:1 ratio and a smoother loss (ε=1e-4).
Key Finding: This model is the undisputed top performer. It surpassed the baseline in less epochs, achieving the best metrics overall: a PSNR of 35.74, an SSIM of 0.962, and the lowest MAE of 11.49. This proves that a sophisticated, multi-stage fine-tuning strategy is the superior methodology.

## Slide 12
sCT generated by Winning Model (E6) :

## Slide 14: Quantitative Results Summary
The performance of each experimental configuration on the test set is summarized in the table below. The "Two-Phase Fine-Tuning" experiment emerged as the clear top performer, achieving the best overall results across all key metrics. This optimized model surpassed the strong performance of the fully-trained 81-epoch baseline model. Notably, the baseline model saved at 54 epochs based on validation loss also showed very strong results, confirming the effectiveness of the standard approach when properly validated.

## Slide 15: Analysis and Interpretation
The Baseline (E1): A standard 81-epoch Pix2Pix model set a strong performance benchmark with a PSNR of 34.75, but required significant training time.
Early Insights: Initial tests showed that an accelerated 3:1 G:D ratio (E3) could speed up early convergence, achieving a respectable PSNR of 33.21 in just 10 epochs.
The Key Innovation: The Charbonnier loss proved to be the most critical factor for efficiency, achieving a high PSNR of 33.81 in only 20 epochs—demonstrating a more effective learning signal than the standard L1 loss.
The Winning Strategy (E6) : A Two-Phase Fine-Tuning approach became the undisputed top performer.

## Slide 16: Conclusion & Key Takeaways
Key Findings : A standard Pix2Pix model with L1 loss provides a strong but time-consuming performance benchmark.The Charbonnier loss was the critical factor for efficiency, enabling the model to learn high-fidelity features much faster than the standard L1 loss.
The optimal configuration was a two-phase fine-tuning strategy, which achieved a new state-of-the-art result (PSNR of 35.74), surpassing the fully-trained baseline in fewer total epochs.
Key Takeaways : The project's main contribution is a novel, superior training methodology. A sophisticated, multi-stage training strategy that combines a stable initial phase with an aggressive fine-tuning period is the most effective path to achieving maximum quality and efficiency for this task.
Future work would be focused on Clinical Validation, Model Optimization and Generalization